## Slide 1
Team Details
Team name -DataNOtfOund
Team leader name -Hitesh Khare
Problem Statement - AI for Smart Cities

## Slide 2
Brief About the Idea — Resonance Fault Detection Platform
⚠ THE PROBLEM
Machines Fail Silently
Bearing wear · misalignment · cavitation — detectable weeks before failure
💀 A single undetected bearing failure stops an entire production line
⏱ Fault signatures appear weeks before catastrophic failure — undetected
🏭 85% of industrial mechanical downtime comes from rotating machinery
🚫 500,000+ Indian SME factories have zero predictive monitoring today
✓ THE SOLUTION
Resonance – Digital Stethoscope
Physics-first · Edge AI · Zero cloud · Any language
🎯 Low-cost piezo sensors + C++ DSP — physics-first detection
🧠 Convolutional autoencoder on AMD Ryzen AI NPU — 4.7ms inference
🌐 Ollama LLM alerts in any language — fully offline, no internet
🏭 Built for 500,000+ Indian SME factories incumbents cannot reach
SIGNAL PIPELINE
PHYSICAL
🎵 Piezo Sensor
35mm disc · contact microphone
1.2MΩ bias · JFET buffer
TIER 1
⚙ DSP Engine
C++17 · PortAudio · FFTW3
44.1kHz · IsolationFilter · ZMQ PUB
TIER 2
🧠 AMD Ryzen AI NPU
ConvAutoencoder · ONNX · Vitis AI
50 TOPS · ~4.7ms inference
TIER 3
🔔 Alert + Dashboard
Ollama LLM · any language · offline
React dashboard · ZMQ :5557
₹3,499
PER SENSOR NODE
85%
CHEAPER THAN SKF
4.7ms
NPU INFERENCE
<1 week
DEPLOYMENT TIME
ZERO
CLOUD DEPENDENCY
500,000+
TARGET FACTORIES

## Slide 3
Market Opportunity & Differentiation
Why Resonance exists — and why no existing solution can serve this market
Incumbents · SKF · Emerson · Schaeffler
₹15,000 – ₹80,000+
/sensor (industry deployment estimates)
+ ₹5–20L/year software · mandatory cloud · 6–18 month deploy
VS
Resonance · Built for SME India
₹3,499
per sensor node · plug-and-play
Installs in <1 week · Zero cloud dependency
Up to
85%
lower deployment cost
vs. incumbent solutions
500,000+
Indian SME factories
85%
downtime from rotating machinery
<3%
currently using predictive maintenance
₹2,491
Per sensor node (Tier 1 BOM cost)
Air-gapped
zero cloud · factory intranet only
WHAT IT TARGETS
⚙ Critical Rotating Machinery
Compressors · Pumps · Motors · Bearings
A single undetected failure stops entire production lines. Rotating machinery accounts for 85% of all industrial mechanical downtime.
HOW IT DETECTS
📊 Physics-First Fault Detection
Bearing wear · Misalignment · Imbalance · Looseness
Spectral signatures from FFTW3 FFT — ISO 10816 / ISO 13373 compliant. No black-box AI — physics validates every alert.
WHY NOW
🛡 The Unserved 97% of Market
SME India · <3% adoption today · Zero cloud needed
Incumbents target enterprise plants. 500,000+ SME factories remain completely unserved. Resonance is designed specifically for them.
"
First offline, physics-first vibration intelligence system built natively for AMD edge AI — designed for 500,000+ Indian SME factories ignored by existing solutions.
* Based on industry deployment ranges; varies by configuration and region.

## Slide 4
List of features offered by Resonance
Real system · Real data · Running on AMD Ryzen AI XDNA NPU
LIVE PROTOTYPE · Resonance Dashboard v1.0
⚙ Signal Processing · Physics-First DSP
High-pass 100Hz + Low-pass 12kHz · C++17 IsolationFilter
2048-pt FFT · 75% overlap · 1024×64 log-magnitude spectrogram
TIER 1
⚡ Deterministic Safety Gate · Hardware Alarm
RMS threshold check — fires independently of AI, cannot be bypassed
Sub-100ms end-to-end · <1ms gate response · ISO 10816
<1ms
🧠 AI Fault Detection · ConvAutoencoder on AMD NPU
Trained exclusively on healthy data · MSE > 0.180
Bearing wear · misalignment · imbalance · looseness · 4.7ms
TIER 2
🌐 Human Interface · Multilingual LLM Alerts
Ollama local LLM · English · Hindi · Marathi · offline
Live waterfall spectrogram · 1× 2× 3× harmonic analysis · React
TIER 3
<100ms
SENSOR→ALERT
2048-pt
FFT SIZE
4.7ms
NPU INFERENCE
Any Language
LLM ALERTS
ZERO
CLOUD DEP
50 TOPS
AMD XDNA NPU

## Slide 5
Process Flow Diagram — Resonance Fault Detection Pipeline
⚙
MACHINE
Physical
A
NODE A
C++ DSP
Pi Zero 2W
B
NODE B
AMD NPU
Python AI
C
NODE C
Engineer
START
Machine
running
Vibration
Bearing motion
→ piezo deflects
Piezo ADC Capture
35mm disc · 1.2MΩ
Logitech USB dongle
PortAudio Stream
44.1kHz · 16-bit PCM
Continuous buffer
⚡ HARDWARE ALARM
Immediate · <1ms
Bypasses AI entirely
↺ continuous
monitoring loop
Isolation Filter
High-pass 100Hz
Low-pass 12kHz
Remove noise
RMS >
thresh?
YES
NO
FFTW3 · FFT
2048-point FFT
75% overlap
512-sample hop
~23ms
Spectrogram Ring
Accumulate 64 frames
Log-magnitude scale
→ 1024×64 tensor
ZMQ PUB :5555
Frame 0: JSON header
{rms,bins,frames,ts}
Frame 1: float32 tensor
✓ NORMAL
No fault detected
Loop back to start
keep monitoring
ZeroMQ PUB/SUB · PORT :5555 · Factory Intranet · 1024×64 float32 tensor + JSON header
Normalize
Apply norm_stats.json
Map tensor to [0,1]
Match training dist.
ConvAutoencoder
Encoder: 3×Conv2d stride 2
Decoder: reconstruct input
Trained on HEALTHY only
AMD Ryzen AI NPU
Vitis AI Runtime
ONNX Exec. Provider
XDNA · 50 TOPS · 15W
~4.7ms
MSE >
0.180?
YES
Ollama LLM
Generate explanation
Any language · offline
EN · HI · MR · others
ZMQ PUB :5557
{mse, rms, severity
alert, spectrogram}
→ Node C
NO
ZeroMQ PUB/SUB · PORT :5557 · {mse, rms, severity, alert} · Socket.IO → Browser
React Dashboard
Node.js · Socket.IO
Live RMS spectrogram
Harmonic Analysis
1× 2× 3× shaft freq
ISO 10816 fault bands
⚠ WARNING STATE
Score + fault explanation
displayed to engineer
Engineer Action
Reads cause · schedules
maintenance
RESOLVED
Fault prevented
Downtime avoided
<1ms
SAFETY GATE
23ms
FFT PROCESSING
4.7ms
NPU INFERENCE
<100ms
SENSOR → ALERT
0.180
ANOMALY THRESHOLD
OFFLINE
ZERO CLOUD

## Slide 6: Wireframes/Mock diagrams of the proposed solution.
Login Screen · Live Dashboard · Node Configuration
● LIVE
RESONANCE · Compressor Bearing — Node 01
RMS: 0.168 · AI ONLINE
LIVE PROTOTYPE · Real data · AMD Ryzen AI XDNA NPU
+ ADD NEW NODE
01 · LOGIN SCREEN
02 · LIVE DASHBOARD
03 · NODE SETUP MODAL
Live Demo
PROTOTYPE
3 Nodes
CONNECTED
50 / zone
CAPACITY
Any Language
LLM ALERTS
Zero Cloud
DEPENDENCY
+ Add Node
INSTANT SETUP
COMPANY LOGIN
▶
▶

## Slide 7
FACTORY INTRANET · AIR-GAPPED · ZERO CLOUD DEPENDENCY
TIER 1 · ZONE A · UP TO 50 SENSOR NODES
Pi Zero 2W
Piezo · ADC
Pi Zero 2W
Piezo · ADC
Pi Zero 2W
Piezo · ADC
ZMQ PUB :5555 · 1024×64 tensor · 5 Hz
C++17
FFTW3
PortAudio
ZMQ
TIER 1 · ZONE B · UP TO 50 SENSOR NODES
Pi Zero 2W
Piezo · ADC
Pi Zero 2W
Piezo · ADC
Pi Zero 2W
Piezo · ADC
ZMQ PUB :5555 · 1024×64 tensor · 5 Hz
C++17
FFTW3
PortAudio
ZMQ
TIER 1 · ZONE C · UP TO 50 SENSOR NODES
Pi Zero 2W
Piezo · ADC
Pi Zero 2W
Piezo · ADC
Pi Zero 2W
Piezo · ADC
ZMQ PUB :5555 · 1024×64 tensor · 5 Hz
C++17
FFTW3
PortAudio
ZMQ
AMD HARDWARE · TIER 2
Ryzen™ AI NPU
Vitis AI · ONNX Runtime · ~4.7ms
ConvAutoencoder · MSE threshold: 0.180
Ollama LLM · any language · offline
AMD HARDWARE · TIER 2
Ryzen™ AI NPU
Vitis AI · ONNX Runtime · ~4.7ms
ConvAutoencoder · MSE threshold: 0.180
Ollama LLM · any language · offline
AMD HARDWARE · TIER 2
Ryzen™ AI NPU
Vitis AI · ONNX Runtime · ~4.7ms
ConvAutoencoder · MSE threshold: 0.180
Ollama LLM · any language · offline
ZMQ PUB :5557 · {mse, rms, severity, alert}
AMD HARDWARE · TIER 3 · PER FACTORY
Mini Server / Edge PC
ROCm — enterprise upgrade path only · Plant-wide health dashboard · Historical archive
Ryzen 5 · 16GB RAM · 2.5 GbE backbone · UPS · ₹72,999 per factory
₹ 72,999/ FACTORY
NODE.JS + REACT · NODE C · BROWSER
Live Dashboard
RMS spectrogram · Anomaly trend · Harmonic analysis · Health score
Ollama LLM multilingual alerts · Multi-node health map
React
TypeScript
Recharts
Docker
SCALE
↕
Add zones
↕
Plug into
same master node
<100ms
SENSOR → ALERT
4.7ms
NPU INFERENCE
50×
NODES PER ZONE
₹3,499
PER SENSOR NOPDE
ZERO
CLOUD DEPENDENCY
50 TOPS
AMD XDNA NPU
Socket.IO
Architecture diagram

## Slide 8
⊿
Powered by H2S
Technologies to be used in the solution
TIER 1 · SENSOR SLAVE
SIGNAL PROCESSING STACK
TIER 2 · AMD NPU INFERENCE
AI & EDGE INFERENCE
TIER 3 · MASTER CONTROL
BACKEND & VISUALIZATION
C++
C++17
DSP core
PA
PortAudio
44.1kHz capture
FFT
FFTW3
2048-pt FFT
ZMQ
ZeroMQ PUB/SUB
intranet relay
π
Raspberry Pi Zero
ARM Cortex-A53
AMD Ryzen™ AI NPU
50 TOPS · 15W
VA
Vitis™ AI Runtime
NPU exec provider
ONNX Runtime
cross-platform infer
PyTorch
Offline model training
LM
Ollama (Local LLM)
Multi-language · offline
Ryzen 5 Edge Mini PC
dashboard + aggregation
Node.js
Socket.IO relay
React + TypeScript
live dashboard
Docker
containerized deploy
Piezo → C++ DSP → ZeroMQ
Raspberry Pi Zero 2W · ₹2,600/node
ONNX → Vitis AI → NPU → Ollama
AMD Ryzen AI · 50 nodes per unit
React Dashboard → Alerts
Ryzen 5 Edge · dashboard + alerts

## Slide 9
POWERED BY H2S
Strategic Usage of AMD Products/Solutions
Native Integration Across Inference and Aggregation Layers
EDGE AI · TIER 2
AMD Ryzen™ AI (XDNA NPU)
FULL-STACK AMD SOFTWARE
AMD AI Software Ecosystem
EDGE COMPUTE · TIER 3
Ryzen 5 Edge Mini PC (Dashboard)
ROLE IN RESONANCE
▸ Runs ConvAutoencoder inference on spectrograms
▸ 4–5ms anomaly detection latency per sample
▸ Serves 50 sensor nodes simultaneously
▸ 15–28W TDP — always-on industrial deployment
AMD SOFTWARE USED
Vitis™ AI Runtime + ONNX Runtime
Vitis AI Runtime — NPU execution provider
ONNX Runtime — Vitis AI EP for inference
AMD NPU Driver Stack — XDNA management
WHY AMD vs ALTERNATIVES
Ryzen AI
50 TOPS ✓
Jetson Orin
ARM only
Core Ultra
No Vitis AI
VITIS™ AI RUNTIME
▸ ONNX execution provider for XDNA NPU
▸ Hardware-accelerated, deterministic inference
▸ Sub-5ms latency per spectrogram
ROCm · OPTIONAL / ENTERPRISE UPGRADE
▸ GPU compute fallback for batch analytics
▸ Historical spectrogram batch reprocessing
AMD uPROF
▸ Edge inference performance profiling
▸ NPU utilization & latency monitoring
AMD SILICON DATA FLOW
Pi Zero
DSP+ZMQ
▶
ZMQ PUB
Ryzen AI
XDNA NPU
▶
JSON alert
Ryzen 5
Dashboard
ROLE IN RESONANCE
▸ Aggregates anomaly data from all Tier 2 zones
▸ Hosts Node.js + React dashboard backend
▸ Stores historical vibration archives on NVMe SSD
▸ Triggers plant-level alerts — SMS, siren, email
AMD HARDWARE
Ryzen 5 7530U Mini PC
6-core / 12-thread — Zen 3 architecture
16GB DDR4 — dashboard + ZMQ relay
256GB NVMe SSD — vibration archive
WHY SEPARATE MASTER NODE
▸ Dashboard isolation — dedicated UI + relay compute
▸ Always-on ZMQ relay — independent from inference node
▸ Fault isolation — NPU failure won't kill dashboard
▸ EPYC recommended for multi-factory · 50+ zones
AMD silicon appears exactly where performance matters — inference (Ryzen AI NPU) and aggregation (Ryzen 5 Edge) — EPYC reserved for multi-factory enterprise scale.
50 TOPS
XDNA NPU
4.7ms
NPU INFERENCE
15–28W
EDGE TDP
₹72,999
MASTER NODE
x86
NO ARM REWRITE
ZERO
CLOUD DEPENDENCY

## Slide 10
TIER 1 — SENSOR NODE
Per machine · Pi Zero 2W
COMPONENT
SPEC
₹ COST
Raspberry Pi Zero 2W
Quad-core ARM @1GHz 512MB
₹1,299
USB Audio Adapter
C-Media CM108 44.1kHz TRRS
₹299
Piezo Disc 35mm
PZT ceramic 35mm dia
₹80
1.2MΩ Bias Resistor
1/4W carbon film ±5%
₹2
1µF Cap (DC block)
25V electrolytic
₹8
2N3819 JFET Buffer
N-ch TO-92 impedance ↑
₹20
TRRS 3.5mm Jack
Panel mount stereo+mic
₹25
MicroSD 16GB
Class 10 OS + software
₹249
5V 2A USB PSU
10W continuous duty
₹249
Enclosure + mount
ABS box neodymium magnet
₹200
PCB + misc wiring
Perfboard solder jumpers
₹60
BOM COST
₹2,491
OUR PRICE
₹3,499
TIER 2 — AMD NPU NODE
Per zone · up to 50 machines
COMPONENT
SPEC
₹ COST
Ryzen AI Mini PC
Ryzen AI 9 HX 370 16GB 512GB
₹74,999
└ AMD XDNA NPU
50 TOPS ONNX + Vitis AI RT
included
└ 12-core CPU
Zen 5 up to 5.1GHz boost
included
└ 16GB LPDDR5X
7500 MT/s dual-channel
included
└ 512GB NVMe
PCIe 4.0 model storage
included
2.5GbE Switch
TP-Link 8-port factory LAN
₹3,499
DIN-rail mount kit
For industrial cabinet
₹999
Power supply (IPC)
12V 5A industrial grade
₹999
Ethernet patch cables
Cat6 3m × 8 per zone
₹800
Software stack
Ubuntu 22.04 Python ZMQ ONNX
₹0 (OSS)
Vitis AI Runtime
AMD official ONNX execution prov.
₹0 (free)
BOM COST
₹81,296
OUR PRICE
₹89,999
TIER 3 — MASTER NODE
Per factory · dashboard + DB
COMPONENT
SPEC
₹ COST
★ Ryzen 5 Edge Mini PC
Ryzen 5 16GB 512GB fanless
₹49,999
└ Role
Node.js + dashboard only
optimal
└ EPYC upgrade
Multi-factory 50+ zones ROCm
₹1,50,000
2TB NVMe SSD
Historical anomaly archive
₹6,999
UPS (600VA)
APC BE600M1 12min runtime
₹4,499
2.5GbE Switch
Industrial ZMQ JSON payload
₹3,499
Software: Node.js
Express Socket.IO ZMQ SUB
₹0 (OSS)
Software: React
TypeScript Recharts Docker
₹0 (OSS)
Database: PostgreSQL
Anomaly history trend data
₹0 (OSS)
Ollama LLM (local)
Mistral 7B offline any lang
₹0 (OSS)
Alert: Email / SMS
Nodemailer Twilio optional
₹0–₹999
BOM COST
₹64,996
OUR PRICE
₹72,999
SME SCENARIO — ASIAN COMPRESSOR
20 critical machines · 2 factory zones · 1 master
20 × Sensor Nodes
Tier 1 @ ₹3,499 each
₹69,980
2 × AMD NPU Nodes
Tier 2 @ ₹89,999 each
₹1,79,998
1 × Master Node
Tier 3 Ryzen 5 Edge Mini PC
₹72,999
Installation
Wiring commissioning setup
₹25,000
TOTAL CAPEX
₹3,47,977
SKF equivalent (20 sensors): ₹9,00,000 + ₹2,00,000/yr cloud
Savings: ₹5,52,023 hardware + ₹2,00,000/yr cloud = ₹7.52L Year 1
REVENUE MODEL — PER 20-MACHINE SME
Hardware sale (one-time)
₹3,47,977
margin: ~20%
Install & commission
₹25,000
margin: ~68%
SaaS: ₹499/machine/month
₹1,19,760/yr
margin: ~85%
Annual maintenance (AMC)
₹35,000/yr
margin: ~70%
Model retraining service
₹5,000/machine
margin: ~90%
YEAR 1 REVENUE
₹5.28 lakh
YEAR 2+ RECURRING
₹1.55 lakh/yr
AMD PRODUCT REFERENCES
Ryzen AI 9 HX 370 (Tier 2 NPU) :
amd.com/en/products/processors/laptop/ryzen-ai/300-series/amd-ryzen-ai-9-hx-370.html
AMD EPYC 9004 (Enterprise Tier 3):
amd.com/en/products/processors/server/epyc/9004-series.html
Vitis AI Runtime (NPU provider):
amd.com/en/developer/vitis-ai.html
Minisforum AI X1 Pro (Mini PC OEM):
minisforum.com/pages/aix1pro
₹3,499
SENSOR NODE (TIER 1)
₹89,999
NPU NODE (TIER 2)
₹72,999
MASTER NODE (TIER 3)
₹3.48L
20-MACHINE SME CAPEX
85%
SAAS MARGIN
₹0
CLOUD COST
Estimated Implementation Cost — Full Component BOM & SME Scenario

## Slide 11: Prototype Assets (Optional)
Demo Video Link (Max: 3 Minutes)
GitHub Public Repository Link : https://github.com/HSKCTA/Resonance

## Slide 12
Powered by H2S
Standing on the
Shoulders of Giants
Every claim is
verifiable.
The same fault signatures defined in ISO 10816 power SKF and Emerson sensors sold at ₹80,000 each. Resonance applies identical ISO-validated physics and peer-reviewed AI — at ₹6,100 per machine.
Proven science.
Accessible price.
3 ISO Standards
4 IEEE Papers
3 Industry Reports
10 verifiable sources on one slide.
EVIDENCE FOUNDATION
⚙ PHYSICS VALIDATED
ISO 10816-3:2009
Defines RMS vibration limits & spectral fault signatures for compressors, pumps & motors. Validates our safety gate.
ISO 13373-1:2002 FFT spectral analysis methods validating 1× 2× 3× harmonic approach.
🧠 AI APPROACH PROVEN
Sakurada & Yairi (2014) · ACM · 500+ citations
Proves autoencoders on healthy data detect anomalies via MSE — exact basis of Resonance.
Principi et al. (2019) · IEEE/CAA
Validates ConvAutoencoder for rotating machinery.
Randall, R.B. (2011)
Cambridge University Press
THE definitive textbook on vibration-based condition monitoring. Defines all spectral fault signatures Resonance detects. SKF cites this directly.
SKF Application Notes
Competitor confirms our physics
World's #1 bearing manufacturer publishes identical spectral signatures in their ₹80,000 sensor docs. Same science. 85% lower cost.
Market Evidence
FICCI 2023 · McKinsey 2022 · Deloitte 2017
500,000 SME manufacturers unserved. $50B/year unplanned downtime. 10× ROI on predictive maintenance. 85% rotating machinery downtime.
"We did not invent new science. We made proven, peer-reviewed, ISO-certified science accessible to 500,000 manufacturers who couldn't afford it."
— Resonance · DataNotFound · AMD Slingshot 2026

## Slide 13
Why Existing Solutions Don't Serve SME Manufacturing
Resonance Targets the Unserved 500,000+ Indian Factories
Feature
RESONANCE
SKF Enlight
Emerson AMS
Schaeffler Optime
Cost per sensor
₹3,499
₹45,000+
₹80,000+
₹25,000+
Deployment time
<1 week
6–18 months
6–18 months
3–6 months
Cloud dependency
None
Mandatory
Mandatory
Mandatory
Works offline
Always
No
No
No
Retrainable AI
Yes
Black-box
Black-box
Black-box
SME accessible
Yes
Enterprise only
Enterprise only
Enterprise only
Local language alerts
Any language
English only
English only
English only
Target market
SME India
Enterprise
Enterprise
Enterprise
Resonance does not compete with incumbents — it serves the manufacturers they cannot reach.
MARKET GAP
500,000+
Indian SME factories
<3%
using predictive
maintenance today
97%
addressable market
gap
Incumbents
target enterprise.
We target the
other 97%.

## Slide 14
Product Roadmap — Resonance Fault Detection Platform
NOW · Q1 2026
LIVE
Batch Inference
& SME Launch
"Is there a fault?"
MODEL · ConvAutoencoder
NPU LOAD · ~20–30% NPU
⚡ Batched NPU inference
50 sensors/zone · 5Hz simultaneous
🔍 ConvAutoencoder
Trained on healthy data · MSE threshold
📊 Harmonic analysis
1× 2× 3× shaft freq · ISO 10816
🌐 Ollama LLM alerts
Any language · offline · no cloud
💰 SME commercial launch
₹3,499/node · ₹499/machine/month SaaS
HW · Tier 3: Ryzen 5 Edge Mini PC
Dashboard + aggregation only
Q2 2026 · 3 MONTHS
NEXT
Fault Type
Classifier
"What kind of fault?"
MODEL · Supervised CNN Classifier
NPU LOAD · ~50–60% NPU
🎯 Multi-class fault labels
Bearing wear · imbalance · looseness
🔬 Lab-simulated faults
Controlled motor obstruction dataset
🧠 2nd model on same NPU
Autoencoder + Classifier in parallel
📈 Severity grading
LOW · MEDIUM · HIGH · CRITICAL
🏭 Mid-market expansion
Up to 100 nodes/zone · larger factories
HW · Tier 2: Same Ryzen AI NPU
No hardware change · software update
Q3 2026 · 6 MONTHS
PREMIUM
Remaining Useful
Life Estimator
"How long until failure?"
MODEL · LSTM on MSE Trend History
NPU LOAD · ~70–80% NPU
⏱ Time-to-failure prediction
"Bearing failure in ~72 hours"
📉 MSE drift tracking
Weeks of trend data → LSTM input
🗓 Maintenance scheduling
Plan downtime before emergency shutdown
💎 Premium SaaS tier
₹999/machine/month · enterprise pricing
🏢 Enterprise Tier 3 upgrade
AMD EPYC 9004 · 50+ zones · ROCm batch
HW · Tier 3 Enterprise: AMD EPYC 9004
Multi-factory · batch ROCm analytics
Q4 2026+ · SCALE
VISION
Multi-Factory
Enterprise Platform
"Which plant needs attention?"
MODEL · Fleet-level Anomaly Network
NPU LOAD · Full NPU fleet
🌍 Cross-factory dashboard
Plant A vs B vs C · central command
🤖 AutoML retraining
Models self-update from field data
🔗 ERP / SCADA integration
SAP · Siemens · Honeywell connectors
☁ Optional cloud hybrid
Air-gapped by default · opt-in sync
📊 Industry 4.0 compliance
ISO 13373 · IEC 61511 · OPC-UA
HW · AMD EPYC + Ryzen AI Fleet
Full AMD silicon stack at scale
Q1 2026
SME LAUNCH · LIVE NOW
50/zone
SENSORS BATCHED (NOW)
~80%
NPU LOAD AT ROADMAP END
3 Models
FAULT DETECTION STACK
₹999/mo
PREMIUM SAAS TIER
EPYC
ENTERPRISE UPGRADE PATH