# 🏗️ PROJECT RESONANCE
Industrial Acoustic & Vibration Anomaly Detection (Edge AI)

# 1️⃣ System Intent
Goal:
Detect abnormal mechanical behavior (bearing wear, imbalance, misalignment, looseness, cavitation) using vibration & acoustic signals on an offline edge device.
The system does not control machines.
It is a diagnostic intelligence layer.

# 2️⃣ Core Principles (Non-negotiable)
Rule	Meaning
Physics-first	Filters and thresholds happen before AI
Deterministic safety	Hard-coded vibration thresholds bypass AI
Advisory only	System never controls machinery
Offline	No cloud dependency
Explainable	All alerts are grounded in signal features

# 3️⃣ Hardware Layer
## 3.1 Sensors
Two signal sources:
Sensor	What it captures
Piezo vibration pickup	Bearing, shaft, gearbox vibration
Air-coupled piezo mic (optional)	Leaks, cavitation, exhaust

These are not industrial-grade accelerometers, but they capture harmonic structure, which is what the AI needs.

## 3.2 Mechanical testbed
A small DC motor with a bearing and shaft is used as a vibration exciter.
Faults are induced by:
- imbalance (tape on rotor)
- misalignment
- loose mounting
- friction load
- synthetic spectral injection

# 4️⃣ Signal Physics
Mechanical faults create frequency signatures:
Fault	Spectral pattern
Bearing wear	High-frequency harmonics
Misalignment	Strong 2×, 3× shaft frequency
Imbalance	Large 1× shaft peak
Cavitation	Broadband noise
Looseness	Sidebands

These exist mostly in:
100 Hz – 10 kHz
Human voice lives in:
80 Hz – 3 kHz
Therefore we do not band-stop — we isolate machine bands.

# 5️⃣ DSP Pipeline (Node A — C++)
### Input
- Audio stream from USB ADC
- Sampling: 44.1 kHz or 48 kHz

### Step 1 — Windowing
Collect:
4096–8192 samples per frame
(~85–170 ms)

### Step 2 — Filtering
Apply:
- High-pass: 100–200 Hz
- Low-pass: 10–20 kHz
Removes:
- DC offset
- wind
- speech
- mains hum

### Step 3 — RMS safety gate
Compute:
RMS = sqrt(mean(signal²))
If:
RMS > CRITICAL_THRESHOLD
→ Immediate alarm (AI bypassed)
This prevents AI missing catastrophic vibration.

### Step 4 — FFT
Perform FFT:
FFT(windowed_signal)
Use:
1024 or 2048 frequency bins

### Step 5 — Spectrogram
Stack FFT frames into a:
Time × Frequency matrix
This is what AI sees.

### Step 6 — ZeroMQ Broadcast
Send:
float spectrogram[time][freq]
via PUB socket.

# 6️⃣ AI Inference (Node B — Python)
## 6.1 Data representation
Each sample is:
[1 × FreqBins × TimeSteps]
Example:
[1 × 1024 × 64]

## 6.2 Model
Convolutional Autoencoder
Trained only on:
Normal vibration
Learns:
What “healthy” looks like

## 6.3 Inference logic
Input spectrogram → Encoder → Latent → Decoder → Reconstructed
Error = MSE(Input, Reconstructed)
If:
Error > learned_threshold
→ Anomaly

## 6.4 Why Autoencoders?
Because:
- Fault data is rare
- Normal data is abundant
- We do not need labeled faults
This is industry-standard for condition monitoring.

# 7️⃣ AI → Human Translation
When anomaly occurs, the system sends:
{ dominant_freqs, rms, error_score }
To a local LLM:
Example prompt:
“Machine shows strong 3× shaft harmonic and rising RMS. Translate this to Marathi for a factory worker.”
Output:
“मशीनमध्ये असामान्य कंपन आढळले आहेत. कृपया तपासणी करा.”
This converts technical DSP → human action.

# 8️⃣ Dashboard (Node C)
Live:
- Spectrogram waterfall
- RMS bar
- Anomaly meter
- Translated alerts
This gives situational awareness, like SCADA.

# 9️⃣ Fault Simulation Strategy
Because real failures are rare:
We inject:
- imbalance
- friction
- load
- software-generated harmonics
This creates:
- known “normal”
- known “fault”
Which trains & validates the system.

# 🔐 10️⃣ Safety & Integrity
Layer	Protection
Sensor	Physical mount
DSP	Deterministic RMS gate
AI	Only advisory
Network	Offline
Control	No actuators

This makes Resonance safe by construction.

# 11️⃣ Why This Is Real Engineering
Resonance matches how:
- SKF
- Siemens
- GE
- Bosch
actually build:
predictive maintenance systems
Your version is a low-cost edge prototype of a billion-dollar industry.

# 12️⃣ What Judges Will See
They will see:
- Live FFT
- Real vibration changes
- AI anomaly scores
- Human-readable alerts
- Offline architecture
- Safety override logic
That is far beyond a toy.

# 13️⃣ What Resonance Actually Is
Resonance is:
A digital stethoscope for machines
Not a chatbot
Not a school project
Not a demo toy
It is:
Edge-AI industrial diagnostics